## Slide 1: Specification in Construction Project
Madhav P. Koirala, Ph.D.
Anjay Kumar Mishra

## Slide 2: Definition and Introduction
It is the document where the level of proposed quality is specified.
Specifications are clear and brief description of materials and workmanship including the methods of construction and precautions to be taken.

## Slide 3
According to http://dictionary.reference.com/browse/specification
The act of specifying.
Usually, specifications are a detailed description or assessment of requirements, dimensions, materials, etc., as of a proposed building, machine, bridge, etc.
A particular item, aspect, calculation, etc., in such a description.
Something specified, as in a bill of particulars; a specified particular, item, or article.
An act of making specific.
The state of having a specific character.

## Slide 4: Specification in Construction Project
It does not include cost, quantity or drawn information.
It to read alongside other contract documentation such as quantities, schedules and drawings.
Also information about materials and workmanship should not on drawings or in bills of quantities.
It depending on the stage to which the design has been developed.
When the project is tendered, ranging from performance (open)specifications that require further design work to be carried out by the contractor, to prescriptive (closed) specifications.

## Slide 5
Prescriptive specifications give the client more certainty about the end product when they appoint the contractor.
If performance specification gives the contractor more scope to innovate, and adopt cost effective methods of work, potentially offering better value for money.
Typically, performance specifications are written on projects that are straight-forward and are well-known building types.

## Slide 6
And prescriptive specifications are written for more complex buildings, or buildings where the client has requirements that might not be familiar to contractors .
An exception to this might be a repeat client such as a large retailer, where a specific, branded end result is required and so along with the building type is well known, the specification is likely to be prescriptive.

## Slide 7
Items crucial to the design will be specified prescriptively (such as external cladding) along with less critical items are specified only by performance (such as service lifts).
Key to deciding whether to specify a building component prescriptively or not is considering who is most likely to achieve best value, the client, the designers or the contractor:

## Slide 8
Large clients may be able to procure certain products at competitive rates themselves (Let us say government),
Some designers may have particular experience of using a specific product .
Although some clients may not allow designers to specify particular products as they believe it restricts competition and innovation and may relieve the contractor of their liability for 'fitness for purpose'.

## Slide 9
Specifications should be developed iteratively alongside the design, and not left until the preparation of production information.
By tender they should describe every aspect of the building in such a way that there is no uncertainty about what the contractor is pricing.

## Slide 10
Aspects of the works are generally specified by:
Products (by standard, a description of attributes, naming (perhaps allowing equivalent alternatives) or by nominating suppliers).
Workmanship (by compliance with manufacturer’s requirements, reference to a code of practice or standards or by approval of samples or by testing).

## Slide 11
It should be possible to verify standards of products and workmanship by testing, inspection, mock-ups and samples, and documentation such as manufacturers’ certificates.
Specifications should be structured according to work packages mirroring the separation of the works into sub-contracts.
This makes it easier for the contractor to price and so may result in a more accurate tender.

## Slide 12: Purpose of Specification
It helps to avoid lengthy description in the bill of quantities and big captions in the drawings.
It supplements information given in the drawings and specification.
It serves the bidders to guide about client’s intended quality requirements and to arrive them at a fair price for the work involved.

## Slide 13
It is a part of contract document between owner and the contractor limiting and describing their risks and responsibilities.
It forms a basis of a contract and it should need to be a comprehensive and precise description of exactly what the client requires.
It serves as a guide for supervisors, engineers and fabricators regarding the methods of construction, fabrication, installation of equipment and materials.

## Slide 14: Need of Specification in Construction Projects
Summary of Work, and other Division sections required by specific project conditions.
For eligible, appropriate projects, shall use the specifications that form part of the annual contract, supplementing those specifications with additional specification sections and keynotes on the construction drawings.
The A/E shall coordinate division specification sections with the requirements in the General Conditions and Supplementary Conditions.

## Slide 15: Types of Specification
Depending upon the purpose served, the specifications can be grouped as follows:
Contract specification is developed for a particular construction or project to accompany the working drawings.
Contract or technical specification is broadly divided in two categories:
  General specification
This describes the nature of the purposed work, qualities of the materials and workmanship in general for the work as a whole

## Slide 16
  Particular specification
This is a detailed written description of every item in the schedule of quantities, which specifies the materials to be used, its quality, workmanship and the results to be achieved.
Usually specification of the items is written in the same sequence as they are mentioned in the BOQ.

## Slide 17
Standard specification
It is prepared and published by national standard organizations which cover specific materials or a group of materials used by a specific trade or a segment of construction industry.
These specifications include methods of manufacture, installation, applications etc.
Standard specifications are usually made project specific by reference.
The Indian Standards Institution has prepared volumes of specification for a wide variety of materials.
These specifications are the result of long and intensive study by experts in the field involved and are generally accepted as authoritative.

## Slide 18
Overall performance specification
This detail in comprehensive but general terms, what the client is looking for.
Manufacturer’s specifications
Manufacturer’s of building product or materials publish specifications of their products or materials describing their quality level, purpose and use.

## Slide 19
Priorities in case of discrepancies
Priced Bill of quantities
Specifications
Drawings
In the event of conflict within drawings, the large-scale details shall govern the small-scale details.
Material Specification and Work Specification

## Slide 20: Specification Writing
The general principles of specification writing are substantially the same regardless of the subject matter, which are as follows:
Specification language - simple and clear. Same tense, repetition of noun is preferable
Brief - as brief as possible.
Standard articles be specified by references and code numbers.
No need to mention reasons of what is specified.
Fairness - fair to all parties. Proper sharing of risk
Express requirement of each and every item
Repetition of information should be avoided to avoid possibility of contradiction
Inapplicable text should not be included

## Slide 21
Inclusion of proper paragraphs
  Specification for materials
  Combination of materials
  Preliminary work prior to construction
  Installation of materials
  Tests, if any
  Clearing on completion
  Mode of measurements
Standard sizes and patterns - commercial sizes should be specified as far as possible, unusual dimensions should be avoided as far as practicable

## Slide 22
Cross references should be as minimum as possible
Quality of materials and workmanship should be specified and not the methodology how that can be achieved.
Nothing impossible to achieve and not intended to be enforced should be specified.
While specifying the brand of materials options and choices should be given.

## Slide 23: General Principle adopted in writing Specification
Specifications must be clear, concise, complete, correct, and consistent.
"Five C's" of good specification writing is provided below.
Clear
Specifications are a tool to communicate an owner's expectations regarding the performance of the work to the contractor.
be clear from its language, and the language should convey only one meaning.
To prevent possible ambiguities, conflicts, and confusion in words and sentence construction, consider the following some points:

## Slide 24
Roles and responsibilities clearly established.
It should clearly indicate the responsibility and authority of both the contractor and the client.
It should be proper use of active voice and imperative mood.
The traditional use of shall and will can also identify responsibility, with shall identifying contractor requirements and will identifying responsibilities of the client and its representative.

## Slide 25
Is all information essential? The requirements and procedures defined should be essential to the client's evaluation of the product for acceptance and payment purposes but are not essential to evaluating product quality or quantity serve no useful function and lead to non-enforcement in the field.
Does the specification exclude expository explanations? Specifications should not explain the reasons for specific requirements.

## Slide 26
Is consistent terminology used throughout the specifications and contract documents, including the Standard Specifications, drawings, and pay items? Terms such as "borrow," "structural fill," and "backfill," should not be used interchangeably on the drawings, specifications, and pay items
Is all terminology defined? All terminology should be defined, particularly terms that have a bearing on the quality of the work or its measurement.

## Slide 27
Has all unnecessary legal and technical jargon been eliminated to the extent possible. Yes
Are requirements expressed using plain and well understood terminology? Words should be used in their true dictionary or technical meaning to avoid conflicts with ordinary or accepted usage.
Does the specification include "escape clauses"? Inclusion of phrases such as "as directed by the engineer," "to the satisfaction of the engineer," or "satisfactory to the engineer," should be limited, as such language does not convey a measurable standard.

## Slide 28
Has all information been provided or otherwise appropriately referenced? The notification should include a contact office and telephone number so the information is available to the contractor, suppliers, and subcontractors.
Are all abbreviations and acronyms defined? Typically, it is best to define abbreviations and acronyms at the time of first use.
Do pronouns clearly refer to a specific noun? If a pronoun could refer to more than one person or object in a sentence, repeat the name of the person or object instead of using the pronoun, or rewrite the sentence to add clarity.

## Slide 29
    Could punctuation cause misinterpretation? Recast the sentence if a change in punctuation might change the meaning.
Are modifiers misplaced? Place words carefully to avoid ambiguity. Keep subjects and objects close to their verbs.
Has all repetition been removed ? Requirements should only be stated once to avoid the possibility of conflicts.
Visually appealing documents are easier to understand than traditional blocks of text and help improve overall clarity.

## Slide 30
    Headings.
    Short Paragraphs.
    Vertical Lists. For example,
      To indicate an OR situation, the list could be introduced with "â€¦one of the following:"
      To indicate an AND/OR situation, one of the following could be used: "one or both of the following:" when one or two items apply in a list of two. "one or more of the following:" when more than one item can apply individually. "one or a combination of the following:" when items can be combined.
      To indicate an AND situation, the lead-in "â€¦all of the following:" would indicate that all items apply.

## Slide 31
Concise.
  Use of the active voice is preferred over the passive voice to directly state essential directions and procedures.
  Short sentences that break up information into smaller, easier-to-process units are better for conveying complex information..
  Eliminate or replace wordy phrases and adjectives and adverbs that do not add to the meaning of the specification.

## Slide 32
Complete
  Specifications should provide the information necessary to enable a bidder to prepare a complete and responsible bid and to enable the contractor to construct the project properly.
  Specifications should be complete and should complement and substantiate the applicable typical sections, dimensions, and details shown on the plans.
  Omissions, ambiguities, or inconsistencies in the plans or specifications are not the responsibility of the contractor.

## Slide 33
Correct
  Specifications should be accurate and factual.
  Sources of data used in the specification should be reliable and current.
  Careless statements or statements based on unreliable data are frequently the cause of contract administration problems and contractor claims.
  Legalistic words and phrases may shorten or clarify specifications, but ensure that usage is correct and that alternate interpretations cannot contradict the intended meaning.
  To ensure specifications are technically correct, research the topic area thoroughly and consult subject matter experts as necessary.

## Slide 34
Consistent
  Consistency in language selection, usage, format, and organization will help prevent conflicts and ambiguities in specifications.
  In addition to the need for consistency in writing specifications, specifications must also be consistently enforced.
  Without consistent enforcement, even a well-written specification becomes ineffective.

## Slide 35
Thank You!